## Slide 1: High Speed Logic Transmission lines

## Slide 2: Transmission lines overview
(1) Characteristics of and applications of Transmission lines
(2) Reflections in transmission lines and methods to reduce them
Appendix1
  Mathematics of transmission lines

## Slide 3: (1) Characteristics of and applications of Transmission lines
Advantages:
  Less distortion, radiation (EMI), cross-talk
Disadvantage
  More power required.
Applications, can hanlde
  Signals traveling in long distance in Printed-circuit-board PCB
  Signals in a cables, connectors (USB, PCI).

## Slide 4: Advantage of using transmission lines: Reduce Electromagnetic Interference (EMI) in point-to-point wiring
Wire-wrap connections create EMI.
Transmission lines reduce EMI because,
  Current loop area is small, also it constraints the return current (in ground plane) closer to the outgoing signal path, magnetic current cancel each other.

## Slide 5: Transmission line problem (Ringing)
Ring as wave transmit from source to load and reflected back and forth.
Solution: Source termination method
or load termination method(see later)
Source
end
Load
end
Source
termination
Load
termination
Long transmission line

## Slide 6: Demo
http://youtu.be/ezGrGXSV3-s
The testing board
Source
Load
Long transmission line (50 )
Source
Load
R=50 
When R=50 
(Matched load)
When R=∞ (open circuit)
Source
32MHz square wave

## Slide 7: Demo
https://www.youtube.com/watch?v=ozeYaikI11g

## Slide 8: Cross sections of transmission lines to show how constant capacitance and inductance per unit length are maintained

## Slide 9
Connector and 50 terminator
Transmission line for cable TV
Cross section of
Coaxial transmission
http://i.ehow.com/images/GlobalPhoto/Articles/5194840/284225-main_Full.jpg
https://en.wikipedia.org/wiki/Category_5_cable
Typical Ethernet Cat-5 cable: characteristic impedance 100 ,
Can carry up to 1GHz of signal
Examples of transmission lines
High voltage Power lines: 115 kV or above, typical characteristic impedance 300 
https://en.wikipedia.org/wiki/Electric_power_transmission

## Slide 10: Characteristic of a transmission line
A transmission line has a Characteristic impedance of Z0
Typically 50 Ohms for a coaxial cable
That means no matter where ( a distance of x meters from the source) you measure the voltage Vx over current Ix at a line is Vx/Ix=50 Ohms
At x,
Z0=Vx/Ix=50 Ohms
Source
Load
ZL
Zs

## Slide 11: (2) Reflections in transmission lines and methods to reduce them
Signals inside the line
(assume the signal frequency  is a constant)

## Slide 12: Define voltages/ functions of the line
A=Vi/Vs= Input acceptance function
T= Vt/Vi=Output transmission function
R2 =Vr/Vi=load-end reflective coefficient
Ii
Ir
Vr
Vt
It
ZL=
Load
Z0
Vi
T=Vt/Vi
R2 =Vr/Vi
Vs
Rs
A=Vi/Vs
R1
Source end
Load end

## Slide 13: Exercises for Transmission lines Exercise 1
Assume a transmission line has a characteristic impedance of 50 Ohms and 10 meters long.
What is the definition of an impedance at a certain point of a circuit ?
At the source end, what is the impedance looking into the transmission line?
At a point X meters away from the source end inside the line, what is the impedance looking at that point? (Give your answers for (i) X=3.2 , and (ii) X=7.6.)
At the load end, what is the impedance looking into the transmission line?
Student ID: __________________ Name: ______________________ Date:_______________
(Submit this at the end of the lecture.)

## Slide 14: Load-end reflection
Load-end reflective coefficient R2
Output transmission function T

## Slide 15: Find Load-end reflective coefficient R2=Vr/Vi
Vt=Vi+Vr
Vi=Ii Z0
Ii- Ir =It (kircoff law)
Vi/Z0-Vr/Z0=Vt/ZL
Vi/Z0-Vr/ Z0 =Vi/ ZL +Vr/ZL
Vr/ Z0+Vr/ ZL = Vi/ Z0-Vi/ZL
after rearrangement, hence
R2=Vr/Vi= [ZL- Z0 ]/ [ZL + Z0 ]
Ii
Ir
Vr
Vt
It
Load
ZL
Z0
Vi
T
R2

## Slide 16: Exercise 2
Assume a transmission line has a characteristic impedance of Z0=50 Ohms and 10 meters long. The source impedance is RS=5 Ohms, and load impedance is RL=70 Ohms.
Draw the diagram of this circuit.
What is the meaning of Load-end reflective coefficient (R2) in English?
Calculate the value of R2 of this circuit.
R2=Vr/Vi= [ZL- Z0 ]/ [ZL + Z0 ]

## Slide 17
R2 in different types of ZL
(case 1) Open circuit at load ZL =
R2=[1-Z0/ ]/[1+Z0/ ]=1
(*The output is doubled; used in PCI bus)
(case 2) Shorted circuit at load, ZL =0
R2,= -1 (phase reversal)
(case 3) Matched line ZL = Z0 =characteristic impedance
R2,= 0 (no reflection) (perfect!!)
Z0
ZL =
ZL =0
(3) Perfect
(1) Output doubled
(2) Signal reflect back
To source

## Slide 18: Exercise 3
Assume a transmission line has a characteristic impedance of Z0=50 Ohms and 10 meters long. The source impedance is RS=5 Ohms, and load impedance is RL=70 Ohms.
If the load end is open,
  what is the value of RL?
  What is the value of the Load-end reflective coefficient (R2)?
  What does this value R2 tell you?
If the load end is closed,
  what is the value of RL?
  What is the value of the Load-end reflective coefficient (R2)?
  What does this value R2 tell you?
If the load end is matched,
  what is the value of RL?
  What is the value of the Load-end reflective coefficient (R2)?
  What does this value R2 tell you?

## Slide 19: Load-end transmission
Output transmission function T

## Slide 20: Derivation for T(): At load-end (Junction between the line and load)
Define
Vt=Vi+Vr
Vt/Vi=1+Vr/Vi
and
T= Vt/Vi=Output transmission function
=Voltage input at load end/ voltage output to load at load end =Vt/Vi
=1+Vr/Vi=1+ load-end reflective coefficient (R2)
Hence 1+ R2=T
Ii
Ir
Vr
Vt
It
Load
Z0
Vi
T
R2

## Slide 21: Output transmission function T=Vt/Vi
1+R2=T=Vt/Vi and
R2=Vr/Vi=[ZL- Z0 ]/[ZL + Z0 ]
Rearranging terms
T=Vt/Vi=1+R2= 2 ZL
[ZL +Z0 ]
Ii
Ir
Vr
Vt
It
Load
Z0
Vi
T=Vt/Vi
R2=Vr/Vi
Vs
Rs
A=Vi/Vs
R1

## Slide 22: Summary of Load-end Output transmission function T
T=Voltage inside line/voltage at load
T=2 ZL /[ZL +Z0 ]
Also 1+R2=T
ZLZ0
Finite length
Characteristic impedance = Z0
Rs
source
Z0
T

## Slide 23: Exercise 4
Assume a transmission line has a characteristic impedance of Z0=50 Ohms and 10 meters long. The source impedance is RS=5 Ohms, and load impedance is RL=70 Ohms.
What is the definition of Output transmission function T?
If the load end is open,
  what is the value of the Output transmission function T?
  What does this T value tell you?
If the load end is closed,
  what is the value of the Output transmission function T?
  What does this value T tell you?
If the load end is matched,
  what is the value of the Output transmission function T.
  What does this value T tell you?
Output transmission function T
T=Vt/Vi=2 ZL /[ZL +Z0 ]

## Slide 24: Source-end reflection
Source-end reflective coefficient R1
Input acceptance function A

## Slide 25: Source-end (R1) reflective coefficient
Source end reflective coefficient =R1
By reversing the situation in the load reflective coefficient case
R1 =[Zs - Z0 ]/[Zs + Z0 ]
ZLZ0
Finite length
Characteristic impedance = Z0
Rs
source
T
R2
A
R1

## Slide 26: Source-end Input acceptance function A
A=Vi/Vs=Voltage transmitted to line/source voltage
A=Z0 /[Zs +Z0 ] , A Voltage divider
Finite length
Characteristic impedance = Z0
Zs
source
ZLZ0
T
R2
A
R1

## Slide 27: Exercise 5
Assume a transmission line has a characteristic impedance of Z0=50 Ohms and 10 meters long. The source impedance is RS=5 Ohms, and load impedance is RL=70 Ohms.
What is the definition of the Source-end Input acceptance function ?
If the source end is 5 Ohms,
  what is the value of Source-end Input acceptance function A?
  What does this A value tell you?
If the source end is matched,
  what is the value of RS?
  What is the value of Source-end Input acceptance function A?
  What is the advantage of this setting (RS= characteristic impedance of the line Z0)?
Source-end Input acceptance function A
A=Vi/Vs=Z0 /[Zs +Z0 ]

## Slide 28: Reflections on un-matched transmission lines
Reflection happens in un-terminated transmission line .
Ways to reduce reflections
  End termination eliminates the first reflection at load.
  Source reflection eliminates second reflection at source.
  Very short wire -- 1/6 of the length traveled by the edge (lumped circuit) has little reflection.

## Slide 29: A summary
A= Input acceptance func=Z0 /[Zs +Z0 ].
T=Output transmission func.= 2ZL/[ZL+Z0]= 1+ R2
R2=load-end reflective coef.=[ZL - Z0 ]/ [ZL + Z0 ]
R1=source-end reflective coef.=[Zs - Z0 ]/[Zs + Z0 ]

## Slide 30: An example
A=Z0 /[Zs+Z0 ]=50/59=0.847
T=2ZL/[ZL+Z0]=2x75/125=1.2
R2=[ZL-Z0]/[ZL+Z0)]
= load-end reflective coef.=75-50/125=0.2
R1=[ZS-Z0 ]/[ZS+Z0]
=Source-end reflective coef.=9-50/59= -0.695
H=Line transfer characteristic0.94 (some loss for many reasons: such as resistance and frequency responses)
75 
15 in. Z0=50 
1V step
9
Transmission line
T
R2
A
R1
A= Input acceptance func.
T=Output transmission func.
R2=load-end reflective coef.
R1=source-end reflective coef.

## Slide 31
Delay=Tp=180ps/in
15in => Tdelay= 2700ps
From [1]

## Slide 32: Exercise 6 : Calculate the following values, plot the figure similar to that in the previous example.
A=Z0 /[Zs+Z0 ]=?
T=2ZL/[ZL+Z0]=?
R2=[ZL-Z0]/[ZL+Z0)]
= load-end reflective coef.=?
R1=[ZS-Z0 ]/[ZS+Z0]
=Source-end reflective coef.=?
H=Line transfer characteristic0.95(some loss for many reasons: such as resistance and frequency responses)
100 
15 in. Z0=75 
1V step
15
Transmission line
T
R2
A
R1
A= Input acceptance func.
T=Output transmission func.
R2=load-end reflective coef.
R1=source-end reflective coef.

## Slide 33: Ways to reduce reflections
End termination -- If ZL=Z0, no first reflective would be generated. Easy to implement but sometimes you cannot change the load impedance.
Source termination -- If Zs=Z0 The first reflective wave arriving at the source would not go back to the load again. Easy to implement but sometimes you cannot change the source impedance.
Short (lumped) wire: all reflections merged when
  Length << Trise/{6 (LC) }
  But sometimes it is not possible to use short wire.

## Slide 34: Application to PCI bus from 3.3 to 5.8V
http://direct.xilinx.com/bvdocs/appnotes/xapp311.pdf
ZL=un-terminated=
T=2ZL/[ZL+Z0 ]=2
So 2.9*2=5.8V
Vin*A=
3.3*70/(10+70)
=2.9V
Line is short (1.5 inches) so
Line transfer characteristic P=1.

## Slide 35: From: http://direct.xilinx.com/bvdocs/appnotes/xapp311.pdf
[The PCI electrical spec is defined in such a way as to provide open termination incident wave switching across a wide range of board impedances. It does this by defining minimum and maximum driving impedances for the ICs output buffers. The PCI specification also stipulates mandatory use of an input clamp diode to VCC for 3.3V signaling. The reason for this is to ensure signal integrity at the input pin by preventing the resultant ringing on low-to-high edges from dipping below the switching threshold. To see this, consider the unclamped case, which is shown in Figure 3. A 3.3V output signal from a 10 ohm source impedance1 into a 70 ohm transmission line will generate an incident wave voltage of 5.8V at the receiving end. After two flight delays, a negative reflected wave will follow, getting dangerously close to the upper end of the input threshold2.]

## Slide 36
Exercise 7
Input= 1 V step
Length L = 10 inches.
Characteristic impedance Z0= 75.
Source impedance RS= 5.
Load impedance RL= 120.
Line transfer characteristic P = 0.9.
Time delay per inch of the line Tp= 160 ps/in.
Sketch the waveform of the signal at the load between the time is 0 and the time when the signal is reflected back to the load end the second time. Mark clearly the time and voltage levels when the signal reaches the load the first time and the second time.
How do you change the values of RL and RS if you want to have a 0.5 V voltage step at the output without ripples?
What is the highest output voltage for all possible RL and RS?
How do you change the values of RL and RS if you want to have a peak of 1.3 V voltage at the output (ripples are allowed)?
Describe with explanation two methods to reduce reflections in a transmission line.

## Slide 37
Answer of Exercise 7 (included for reference)
Similar to the example discussed.
How do you change the values of RL and RS if you want to have a 0.5 V voltage step at the output without ripples? (answer: two methods (i) set Rs=Z0 for no source reflection, RL=93.75 Ohms. (ii) set RL=75 Ohms , no load reflection, Rs =60 Ohms)
What is the highest output voltage for all possible RL and RS? ANS:(RS=0, RL=infinity) Vout=p*Tmax=0.9*2V
How do you change the values of RL and RS if you want to have a peak of 1.3 V voltage at the output (ripples are allowed)? ANS: p*T=0.9*2*RL/(Z0+RL)=1.3, (Rs=0, RL=195). You may use a smaller value for RS similar to the PCI bus, say 10 .

## Slide 38: Conclusion
Studied Characteristics of transmission lines.
Studied ways to terminate the line to avoid reflection.

## Slide 39: References
[1]Chapter4 of High speed digital design , by Johnson and Graham
[2] Kreyszig, Advanced Engineering maths, edition 6, Page 74
[3] Buckley, Transmissions networks and circuits , The Macmillan press. Page 1
[4]http://direct.xilinx.com/bvdocs/appnotes/xapp311.pdf (For PCI application)

## Slide 40: Appendix 1

## Slide 41: Mathematics of transmission lines

## Slide 42: Main formulas (for proof, see appendix 1)
If  = [(R+ j  L)(G+j  C)]
V=Ae-x +Bex ----------------------(13)
I=(A/Z0)e-x - (B/Z0)ex ------------(14)
Z0= [(R+j  L)/(G+j  C)]=characteristic impedance

## Slide 43: Incident and reflective waves
Vx=Ae-x +Bex
Ix=(A/Z0)e-x -(B/Z0)ex
 = [(R+ j  L)(G+j  C)]
Z0= [(R+j  L)/(G+j  C)]=characteristic impedance
Incident wave
Reflective wave
Source
termination
Load
termination
Long transmission line (characteristic impedance Zo, typically = 50 Ohms)
x
Vx=voltage at X
Ix=current at X

## Slide 44: Characteristics of ideal Transmission lines
Ideal lossless transmission lines
  infinite in extent
  signals on line not distorted/ attenuated
  but it will delay the signal measured as picoseconds/inch, this delay depends on C and L per unit length of the line. (by EM wave theory)
  Delay (ps/in)=10+12 [(L per in)*(C per in)]
  Characteristic impedance = [L per in/C per in] 

## Slide 45: Appendix 1
Math of transmission lines

## Slide 46: Characteristics of ideal Transmission lines
Ideal lossless transmission lines
  infinite in extent
  signals on line not distorted/ attenuated
  but it will delay the signal measured as picoseconds/inch, this delay depends on C and L per unit length of the line. (by EM wave theory)
  Delay (ps/in)=10+12 [(L per in)*(C per in)]
  Characteristic impedance = [L per in/C per in] 

## Slide 47: Step response of transmission lines
(by EM wave theory)

## Slide 48: Delay and impedance of ideal transmission lines
Step (V) input to an ideal trans. line (X to Y) with C per in =2.6pF/in, L per in =6.4nH/in .
Cxy=(C per in)(Y-X)
Charge held (Q)= Cxy V=(C per in)(Y-X)V
Per unit length Time delay (T)=(Y-X) [(L per in)(C per in)]
Current=I=Q/T
I= (C per in)(Y-X)V = V* (C/L)
{(Y-X){[(L per in)(C per in)]}1/2
Z0=V/I= (L per in /C per in ) =(6.4 nH/2.6 pF) 1/2 =50
By EM wave theory

## Slide 49: A quick reference of the important transmission line formulas
V= Ae-x + Be +x
I = (A/Z0)e-x - (B/Z0)e +x
Where A, B are constants.
Z0 =characteristic impedance is real.
 = propagation coefficient is complex
Derivations will be shown later

## Slide 50: A small segment
R=resistance; G=conductance; C=capacitance; L=inductance. All unit length values.
i
R x L x
G x
C x
x
v
For a small segment x
A long transmission line
v

## Slide 51: For the small segment of wire
--(horizontal voltage loop)
-(v/ x) x=R x i + L x ( i/  t)
--(vertical current loop)
-(i/ x) x=G x v + C x ( v/  t)
-(v/ x)=Ri+L( i/  t) ------------------(1)
-(i/ x)=Gv+C( v/  t) ------------------(2)
Applying phasor equations, I,V depend on x only , not t
v=Vej  t --------------------------------------(3)
i=Iej  t ----------------------------------------(4)

## Slide 52: Applying phasor equations, I,V depend on x only, not t But v,i depend on t and x v = Vej  t ---------------------------------------(3) i = Iej  t ----------------------------------------(4)
Hence from (3) and (4)
(v/ x)= ej t(d V / d x) --------------------(5) (v/ t)= j  V ej t--------------------------(6)
(i/ x)= ej t(d I / d x) ----------------------(7)
(i/ t)= j  I ej t----------------------------(8)
Since in general,  ekt / t = k ekt

## Slide 53: Put 5,4,8 into 1
-(v/ x)=Ri+L( i/  t) -------------(from 1)
-(dV /d x )ej t = R I ej t + L j  I ej t
-(dV /d x ) = (R+j  L)I --------------------(9)
=> -(d2V/dx2)=(R+j  L)dI/dx
= -(R+j  L)(G+j  C)V
(d2V/dx2) = +2V --------------------------(11)
where  = [(R+ j  L)(G+j  C)]
(10, see next page)
(4)
(8)
(5)

## Slide 54: Put 7,3,6 into 2
-(i/ x)=Gv+C( v/  t) ------------(from 2)
-(dI /d x )ej t = G V ej t + Cj  V ej t
-(dI /d x ) = (G+j  C)V-----------------(10)
=> -(d2I/dx2)=(G+j  C)dv/dx
= -(G+j  C)(R+j  L)I
(d2I/dx2) = + 2 I --------------------------(12)
where  = [(R+ j  L)(G+j  C)]
(9, see previous page)
(7)
(3)
(6)

## Slide 55: From the wave equation form (see [2] , Homogeneous 2nd order differential equations, also see appendix2,3)
(d2V/dx2) = 2V -------(11)
(d2I/dx2) = 2 I ---------(12)
where  = [(R+ j  L)(G+j  C)]
Solution is
V=Ae-x +Bex ----------------------(13)
Differentiate (13) and put into (9), see appendix 2
I=(A/Z0)e-x - (B/Z0)ex ------------(14)
Z0= [(R+j  L)/(G+j  C)]=characteristic impedance

## Slide 56: Different transmission lines
(Case 1) Infinite transmission line; impedance looking from source is the characteristic impedance Z0.
(Case2) Matched line (finite line with load connected to Z0) has the same property as an infinite transmission line
(Case3) unmatched line : reflection will occur

## Slide 57: (Case1) Infinite transmission line
For Infinite line, the impedance is the characteristic impedance Z0

Impedance
looking
from
source=
Z0
Characteristic impedance = Z0

## Slide 58: Infinite transmission line: characteristic impedance= Z0
Vs is driving an infinite length trans. Line
Since Vx=Ae-x +Bex
At x=0, V0=Vs= Ae0 +Be0=A+B
AT x= ,V  = Be =0 (so B =0, meaning no reflection occurs at infinite line)

Vs
X=0
V0
At x= , V  =0

## Slide 59: Infinite transmission line: characteristic impedance= Z0
Vs is driving an infinite length trans. line
At source position X=0,V=Vs=Ae0+Be0
At X=infinity, V0 voltage is completely attenuated. 0=Ae-x+Be +x,
The only solution is B=0, A=Vs(no reflection)
Hence V=Vse-x , I= (Vs/Z0)e-x,
V/I= Vse-x / (Vs/Z0)e-x = Z0=characteristic impedance (a constant)

## Slide 60: (Case 2) Matched line (no reflection)
A finite length line with characteristic impedance Z0 is connected to a load of Z0. It has the same property as an infinite transmission line (**no reflection)
Same as
infinite line:
Impedance
looking
from
source=
Z0
Z0
Finite length
Characteristic impedance = Z0

## Slide 61: Matched line, characteristic impedance= Z0 (Same as infinite line, no reflection)
Matched line
  Infinite line input impedance = Z0
  A finite length line terminated by Z0 is matched line, it also has the same property as infinite lines. Therefore V=Vse-x , I= (Vs/Z0)e-x,
un-matched line is different, it has reflections inside.
Z0
Zo
Infinite line
l
l
Zo

## Slide 62: Appendix2: 2nd order homogenous differential equation
Page 74 of [2], use ()’=d /dx
y’’+ay’+by=0 ------(i)
Put y=ex ,hence (1) becomes
(2+a +b) ex =0,
The solutions for the equation (2+a +b) are
1=(-a+[a2-4b]1/2)/2 and 2=(-a-[a2-4b]1/2)/2
The solutions to (1) are y1=e 1x and y2=e 2x
The general solution is y=Be 1x +Ae 2x , find constants B,A from boundary conditions.

## Slide 63: Appendix2 continue: Our transmission line equation
The standard form is y’’+ay’+by=0 ------(i)
Our equation is (d2V/dx2) = +2V
Solutions for (2+a +b) or (2 -2)=0,
where a=0, b= -2
1=(-a+[a2-4b]1/2)/2 =(-0+[02+42]1/2)/2= 
2=(-a-[a2-4b]1/2)/2 =(-0-[02+42]1/2)/2= -
The solutions to (i) are
y1=e x and y2=e -x
The general solution is y=Bex +Ae-x, find B,A from boundary conditions.

## Slide 64: Appendix 3, from ref. [3]
-(dV /d x ) = (R+j  L)I --------------------(9)
V=Ae-x +Bex ----------------------(13)
Differentiate (13) w.r.t. dx
dV/dx=-Ae-x +  Bex, put this into (9), hence
(R+j  L)I= Ae-x -  Bex
I= (Ae-x -  Bex)/ (R+j  L)
I=(A/Z0)e-x - (B/Z0)ex
Since  = [(R+ j  L)(G+j  C)]1/2 and
Z0= [(R+j  L)/(G+j  C)]1/2